## Slide 1
terralabs
terra labs
terra labs
Tether Kickoff
fall 2026 · sep 27

## Slide 2
welcome to

## Slide 3: today
where this project comes from, where it's going, and how we get there
01
who we are
your two PMs
02
cove
the 7-DOF arm we built last spring
03
tether
turning cove into an inchworm
04
the sim
what's already built in software
05
the plan
roadmap, open questions, first week

## Slide 4: pm introductions
two of us: one on hardware, one on software
John Peng
hardware PM
ECE sophomore at USC. worked on cove's controls: ROS 2, CAN, MIT-mode torque control, e-stop logic. leads mech + electrical on tether.
Steve Lu
software PM
leads tether's software: the sim, motion planning, and the controls stack that runs on the robot.

## Slide 5
terralabs
spring 2026
cove
where we're starting

## Slide 6: cove: the goal
7 joints, Z-X-Z-X-Z-X-Z, symmetric so the same parts could become an inchworm
day zero: sketch it, check reach and torque, start ordering that night
the target: grab the bottle, pour, release
build a 7-DOF arm from scratch that can pick up and pour a wine bottle

## Slide 7: cove: how we built it
every part pre-sized from stress spreadsheets, then modeled in OnShape
printed every part first to get fitment right. plastic is cheap
1 week on a 3-axis mill: 8 aluminum parts from 3 pieces of stock, $308
size it on paper → CAD → print everything → machine to aluminum

## Slide 8: cove by the numbers
what the finished arm could do
7
joints on one CAN bus
≈50 Nm
working torque budget
≈7 kg
payload at full reach
$308
aluminum stock for 8 parts
full assembled arm, before wires

## Slide 9: cove: electronics
7 Damiao actuators with built-in encoders + torque sensing, daisy-chained on CAN
Raspberry Pi host, CAN/UART bridge, hardware e-stop on motor power
24 V power trunk down the arm (XT-60/XT-30), cables routed with slack
one CAN bus, one power rail, one host computer

## Slide 10: cove: software
URDF exported from OnShape → RViz + MoveIt2 for IK and joint commands
camera reads AprilTags → target pose → MoveIt2 plans → CAN → motors
electromagnet end effector: no gripper roll to solve, one less thing for IK
ROS 2 on a Raspberry Pi, MoveIt2 for planning, AprilTags to find targets

## Slide 11: cove: the disaster
the thread that let go
4 broken actuators, blown fuses, fried CAN ports
stripped holes at the base
apr 26: the bottom threads failed under load and the arm fell. we rewired and rebuilt it

## Slide 12
terralabs
fall 2026
tether
where we're going

## Slide 13: tether: the idea
inspiration: GITAI's IN1, an inchworm arm with grapple end effectors on both ends
no fixed base and no cable to a wall: everything rides on the arm
cove's joint chain is symmetric, so either end can be the base
put a gripper on both ends of cove and let it walk: one end holds on, the other moves
1
A holds on, B swings forward
2
B grabs the next spot
3
A lets go
4
A swings forward, repeat

## Slide 14: what changes from cove
 | cove (spring) | tether (fall)
base | bolted to a base plate | none: either end can anchor
end effectors | electromagnet on one end | a gripper on both ends
power | 24 V, 240 A bench supply | onboard battery + BMS
wiring | cables with slack, rotation limited by wiring | slip rings or managed cable winding
compute | Pi on the arm, visuals on a laptop over SSH | onboard, in a closed package
the task | pour a wine bottle | walk, climb, and still manipulate
the tether column is the plan, and most of it is still open. that is what this team is for.

## Slide 15: what's already built in software
COVE2 Robot Studio: test the design in a browser before we cut metal
motion replay: inchworm climbing the ladder, every frame collision checked
works today
editor built on cove's real URDF
two-ended FK/IK: drive either end
PyBullet collision checks on every motion
motion search: walk → ladder, table loop, task programs
not yet
trained RL (the RL worker is a test harness)
contact, friction, and torque limits
collision geometry checked against the real arm

## Slide 16: three ways to route wires through the joints
inchworm (slip rings): walked 1.08 m, climbed all 5 rungs
cable 360 (±360° joints): hit the twist limit before the ladder
existing (cove as built): J4 hit its 145° limit at the ladder
same motions in the sim: only inchworm climbed the ladder and closed the table loop
from today's run of the repo sim on cove's URDF, with an assumed ±0.5-turn cable budget. not validated against hardware yet.

## Slide 17: roadmap (draft)
software de-risks the design while hardware bench tests the parts, then they meet
software
G0
model freeze: audit cove vs URDF
G1
kinematic feasibility
G2
scripted dynamics
G3
contact + RL robustness
hardware
G4
gripper pull-off test
G4
battery + BMS bench test
G4
slip ring / cable rotation test
G4
compute thermals + motor watchdogs
G5
integrated locomotion
first supported steps on the real robot, compared against the sim logs
done in sim
started
next
rough timing: G0 + G2 in the first month, G3 and the G4 bench tests mid-semester, first G5 steps by the end. we set real dates together.

## Slide 18: big open questions
the problems this team gets to solve
01
the grippers
what do both ends grab, and how hard? rungs, table edges, scaffold members
02
wires through joints
slip rings or managed cable winding. the sim already says this decides what motions are possible
03
power on board
a battery + BMS riding on the arm, and the weight that comes with it
04
lifting itself
cove held a payload off a fixed base. tether holds up its own body from either end
05
compute on board
a Pi in a closed package: heat, comms, watchdogs
06
sim to real
the URDF isn't hardware truth yet. audit cove, then trust the sim

## Slide 19: where we are
cove is built and moves. tether exists in the sim: on cove's model it can plan a collision-free walk, a ladder climb, and a loop around a table. nothing physical for tether exists yet. that's this semester.
first two weeks: everyone gets the sim running, hardware audits cove against the URDF (G0), and we pick gripper concepts to bench test.
what’s next

## Slide 20
terralabs
terra labs
terra labs
questions?